## Slide 1: GPSC_LIM food web
Part 2: Model construction

## Slide 2
Development of a linear inverse model

## Slide 3
Development of a linear inverse model
doc_w
dic_w
det_w
det
doc
bac
nem
mac
exp
f1
f2
f3
f4
f5
f6
f7
f8
f9
f10
f11
f12
f13
f14
f15
f16
f17
All mass balances are assumed to be in steady state

## Slide 4
Development of a linear inverse model
All mass balances are assumed to be in steady state (i.e. b=0)
A
x
b
5 x 17
17 x 1
5 x 1
Unknown flows

## Slide 5
Topological food web structure
SYM | MEANING
POC->SED | Organic matter derived from the water column
SED->EXP_S | Sediment export(e.g. downslope, burial…)
SED->BAC | Bacteria feed on detritus OC
BAC->SED | Bacteria feces deposit on sediment
SED->MEI | Meiofauna feed on detritus OC
MEI->SED | Meiofauna feces deposit on sediment
SED->MAC | Macrofauna feed on detritus OC
MAC->SED | Macrofauna feces deposit on sediment
BAC->MEI | Meiofauna feed on bacteria
BAC->MAC | Macrofauna feed on bacteria
MEI->MAC | Macrofauna feed on meiofauna
MEI->EXP_B | Meiofauna predated by other benthopelagic/pelagic predators
MAC->EXP_B | Macrofauna predated by other benthopelagic/pelagic predators
BAC->DIC | Bacteria respiration
MEI->DIC | Meiofauna respiration
MAC->DIC | Macrofauna respiration
abiotic
biotic
Internal flows
Exchange with external

## Slide 6
Ax=b
Mass conservation
abiotic
biotic
Internal flows
Exchange with external

## Slide 7
Directly use measured TOU data
Dealing with respiration problem
LSEI error: inequalities contradictory
  Using equalities and/or inequalities that are incompatible.
  eg.: I want that a > 10 but also that a < 2
LSEI error
Only assume maintenance respiration
(van Oevelen)
Use speculated respiration rate
Calculated based on allometric relationships and temp (Mahaut et al 1995)
Successfully run
Compare results

## Slide 8
Dealing with respiration problem
Only assume maintenance respiration (MR)
(van Oevelen)
Use reference respiration rate
Calculated based on allometric relationships and temp (Mahaut et al 1995)
A. Weight-dependent respiration rates:
  BIO->DIC (R) = 7.4*10^-3*Stock(W)^(-0.24)
  ! Exponential function is not allowed in LIM.input file, so R is calculated base on the initial stock (this is not a dynamic model)
B. Maintenance Respiration(mr)= Tlim * 0.01 * STOCK
  Maintenance costs are taken proportional to 1% of the biomass per day (Fenchel, 1982; Nielsen et al., 1995)
Growth respiration(gr)= BIO->DIC-mr
Other processes
  Assimilation efficiency (AE)= (Consumption-Defecation)/Consumption
  Net growth efficiency (NGE)=(Consumption-Defecation-gr)/ (Consumption-Defecation)
  (Consumption-Defecation-gr)/Stock= P/B ratio
C. BIO->DIC= biomass-specific faunal respiration rate (bsFR)*Stock

## Slide 9
SSA Result:
LSEI error
BAC: 30% of TOU
MEI: 7.4*10^-3*MEISS^-0.24
MAC: 7.4*10^-3*MACSS^-0.24
→ set less limits
→ keep:
MEI: 7.4*10^-3*MEISS^-0.24
MAC: 7.4*10^-3*MACSS^-0.24 →problem unsolved

## Slide 10
SSA Result:
→ keep:
BAC: 30% of TOU

## Slide 11
SSA Result:

## Slide 12
SSA Result:
Tlim = Q10* exp((T-20)/10), with Q10 = 2
Station | Bottom water temperature(°C) | Tlim
GC1 | 13.54 | 1.05
GS1 | 13.90 | 1.09

## Slide 13
SSA Result:
LSEI error
BAC: 30% of TOU
MEI: 7.4*10^-3*MEISS^-0.24
MAC: 7.4*10^-3*MACSS^-0.24
→ set less limits
→ keep:
MEI: 7.4*10^-3*MEISS^-0.24
MAC: 7.4*10^-3*MACSS^-0.24 →problem unsolved

## Slide 14
SSA Result:
→ keep:
BAC: 30% of TOU

## Slide 15
SSA Result:

## Slide 16
SSA Result:
Tlim = Q10* exp((T-20)/10), with Q10 = 2
Station | Bottom water temperature(°C) | Tlim
GC1 | 13.54 | 1.05
GS1 | 13.90 | 1.09

## Slide 17
SSA Result:
Summary (for both GS1 and GC1 model):
Direct use TOU data -> LSEI error
Include BAC (=30% TOU) and MAC/MEI(=7.4*10^-3*Stock^-0.24) respiration data->LSEI error
Only include BAC (=30% TOU) data -> successfully run
Use literature respiration rate -> successfully run
Use maintenance respiration rate -> successfully run
Results of (3) and (5) are the same->combine 2 input file to one
Compare (4) and (6) -> no difference

## Slide 18
Before compare results from different methods
if the number of iterations is high enough to produces convergence of the mean and the standard deviation
  standard deviation < 2%
  Check at least 3 different magnitude flows
if the range of sampled values cover the range of possible solutions
  >75% of the flows has a sampled range of >75% of the solution range
Iteration=10000; jumpsize=100

## Slide 19
LA Result:
if the range of sampled values cover the range of possible solutions?
  Mean sample coverage: 83.28

## Slide 20
if the number of iterations is high enough to produces convergence of the mean and the standard deviation?
  standard deviation < 2%
  Check at least 3 different magnitude flows

## Slide 21
LA Result:
if the range of sampled values cover the range of possible solutions?
  Mean sample coverage: 77.51

## Slide 22
if the number of iterations is high enough to produces convergence of the mean and the standard deviation?
  standard deviation < 2%
  Check at least 3 different magnitude flows

## Slide 23
Remove POC->SED (same value was set for 2 sites)

## Slide 24
2022.02.11 Meeting
ANOVA: is there seasonality difference between GC1 and GS1?
  Yes -> make different season models
  No -> used to defend why we only take the mean of biomass data
Figure out the meaning of negative value in parsimonious method
  If necessary, change the structure
Check different sedimentation rate in other paper (maybe with seasonal one)/ or use our TOC content to see if there’s difference in input value

## Slide 25
20220322_Fix burial problem
原本: calculate POC_W->SED，讓model 算burial
結果: lsei problem
新方法: calculate accumulation (體積*our TOC% ) and set as a constant，讓model 算POC
(Huh et al., 2009)
Average sedimentation rate in the upper slope region (200–600 m) is 0.43 g cm2 yr1->GS1
higher mass accumulation rates (>1.0 g cm2 yr1 ) ->GC1 (flanking the Gaoping submarine canyon over the upper slope region at a water depth 300 m.) This high deposition area corresponds to the area characterized by flood sedimentation.
Steps:
1. Convert g/cm2/y -> g/m2/d (by *10000/365)
2. Calculate measured TOC(in %->/100) mean and sd
3. g/m2/d * TOC *1000=mg C/m2/ d

## Slide 26
GC1
GS1